Motorcycle aerodynamics.

You need about  a  couple of million quid  a year to run a top bike team. For even an also-ran  F1  car operation,  the figure is a couple of million quid a WEEK. So if you run  a bike racing set-up, you must spend what little money you have  on

really  important  things, like flash paddock jackets and  a  big

motorhome.  Aerodynamic research  comes a long way down the  list

of priorities.

I spent a  year at  Cranfield  Institute researching high  speed  ground  vehicle

aerodynamics  and designing a land speed record car body  in  the

moving ground-plane wind tunnel there.

The  deal was that if I hung around outside the wind tunnel  with

my  scale model all instrumented up and ready to go,  they  would

let  me  in  to do some tests if the F1 team of  the  day  either

didn't  show, or packed up early for some reason. They didn't  do

this too often, as the tunnel was booked solid a year in advance.

The tunnel rent, by the way, was £1500 per day, but that was hardly

big biccies to an outfit with a few million a week to spend.

As  far  as  I  know,  no bike  team  has  ever  even  telephoned

Cranfield  about using one of the wind tunnels. During the  whole

of  my  stay  there,  the only  bike  seen  in  the  Aerodynamics

Department  was  my Suzuki TS125 trailbike.

My  studies  at  Cranfield  showed  me  just  how  important  the

management  of the airflow around and through a vehicle  can  be.

What surprised me was that many basic rules can be applied to any

vehicle -  plane, car, locomotive, or bike. Then I looked around,

and  couldn't  understand  why so few racing  teams  were  taking

advantage  of all of this knowledge, when it  really  represented

"free" horsepower, and could help  handling too.

You would be surprised how even the most trivial modification can

have a big effect on the drag, and therefore the top speed. Stick

your  hand  out  from behind the fairing at 80mph  and  you'd  be

shocked  at  the  amount of force on it. Working it  out  with  a

pencil  and paper (like the constipated mathematician)  I  reckon

the  force  would  be  about equal to  a  constant  loss  of  one

horsepower.  The cube law applies here, so at 160mph (double  the

speed) the equivalent power loss would be 2 x 2 x 2 this  amount,

8bhp.

Having established that there are real gains to be made from  the

application  of aerodynamic theory to bikes, it is worth  looking

at a few basics. The most basic issue of all is, of course,  what

the rulebook says you can do. The regulations are worded in quite

a  loose  way, and allow a fair scope for  experiment,  but  only

within clearly defined limits.

One  reason for this is perhaps historical. In the 1950s  several

attempts  were  made at all-enclosing "dustbin"  fairings,  which

were   blamed  for  a  couple  of  serious  accidents. Ever since then, the rules have decreed that  the front wheel (but not necessarily the tyre) must not  be

covered  by  bodywork, so that it is clearly  visible  from  each

side,  though the regulations about front mudguards are not  very

strict.

Aerofoils (wings) are allowed, but they cannot be wider than  the

bodywork,  nor  higher  than the handlebars. The  rider  must  be

clearly visible from the sides and from above, and no fairing  is

allowed  within  100mm of his body (this is  often  ignored).  An

anti-smartarse rule prohibits the use of perspex bodywork to  get

around the "clearly visible" bit.

Now to some basic aerodynamic theory. For a start, the drag of  a

vehicle depends on its size (strictly its frontal area), and  its

shape.  The  measure  of how much drag a  particular  shape  will

produce  is called the Drag Coefficient or Cd.

A very high-drag shape like the gloved hand being stuck out  from

behind  a  fairing will have a Cd of about 1.1,  and  a  low-drag

shape  (like the famous teardrop which everyone keeps  on  about)

will have a Cd below 0.2. Passenger cars are about 0.4, bikes are

in  the  0.7 area, and F1 cars (with their  barn-door  wings  and

tyres  like paint rollers) are well over 1.0. Note that  size  is

just as important as shape so  a big shape with a low Cd can have the same total drag  as  a small shape with a high Cd if the numbers happen to come out  the

same.

Much  tosh is talked about "laminar" and "turbulent" flow, and  I

had  better give a proper explanation of the terms. For a  start,

the  flow  around  a racing bike is well  turbulent.

The correct application of the words "laminar" and "turbulent" is

to the "boundary layer" which is that part of the airstream close

enough  to  the bike body to be dragged along by it.

Air  has  a  certain viscosity, it's not exactly  in  the  15W/40

league,  but is big enough to be measured.  So the layer  of  air

molecules  next to the bike body sticks to it, and  therefore  it

has  to travel along with the bike. The layer of molecules  above

that  is dragged along slightly more slowly, and the layer  above

that  slightly more slowly again, and the layer above that,  etc,

until  you  get out of the air pocket that the  bike  is  pulling

along. Note that this is much smaller than the area of air  which

the bike disturbs as it goes by.

The  edge  of the boundary layer is defined as  being  where  the

velocity  of  the air relative to the moving body is 99%  of  the

relative velocity of the undisturbed air further away.

The thickness of this boundary layer at any point depends on  how

fast the body is moving, and how far the point is from the  front

of  it. Boundary layers near the front of slow vehicles are  thin

and  laminar, but they will turn turbulent when they get  thicker

at  a  certain  combination of airspeed,  position,  and  surface

roughness.

This is not a bad thing at all, as flow tends to attach itself to

a  body  better if there is a turbulent boundary layer.  You  can

frequently  see  exactly where flows turn  turbulent  on  various

things by the patterns left on mucky surfaces. Flow detachment is

the  ultimate  enemy  which  must be avoided  at  all  costs,  as

explained later. (See fig 1).

During  wind-tunnel tests, it is critical to know  exactly  where

the  boundary layer goes turbulent as the experiment will not  be

much use if the model behaves differently from the full-size set-

up.

You  can  do this by spraying the model with  special  paint  and

seeing  what surface texture it produces when you turn  the  wind

on,  but  this is a bit messy. My favourite method was to  put  a

hypodermic needle connected to a doctor's stethoscope up  against

the model. Where the boundary layer is laminar, the sound is like

a child blowing through a drinking straw, but turbulent  boundary

layers sound like a distant jet engine roar. The difference is so

obvious that you can draw the transition line on the model with a

felt-tip pen.

You  can  often make boundary layers which should be  laminar  go

turbulent  by gluing what is known as a "trip" to the surface  of

the  body, normally just a piece of cotton or a narrow  strip  of

sandpaper  will  do it. It is possible to see much  more  radical

attempts at keeping surface flow energised on aircraft. There  is

a  row of little vortex-generating teeth a couple of inches  high

along  the top of a Harrier wing, for example. They are there  to

keep  the  flow attached to the wing surface at  high  angles  of

attack and low speed.

Detached  flow means that the air no longer follows the  line  of

the  body, making a huge air pocket instead that the vehicle  has

to  drag along like an invisible parachute.

Flow  will detach from the lip of a bike screen, and  then  often

fail to reattach itself to the rider's back or the seat  fairing.

In  this event, instead of tucking in as tightly as  possible,  a

clued-up  rider can find extra speed by raising his backside  off

the  seat  slightly until the flow sorts itself out  -  when  the

effect  can  be  seen on the rev-counter.

Flow will attach and detach itself at various speeds depending on

the  particular  circumstances. It is  practically  impossible  to

predict exactly when it will happen.

Ian  Botham, retired cricket hero, used to provide a fine example of flow attachment  in action. He developed a technique of bowling the ball at  slightly

above the speed at which all the flow is attached, about 75mph in

that  particular case. When the ball had slowed down a  bit,  the

flow  would suddenly detach itself, but only on the side  of  the

ball  not  affected by the seam. This meant that the  ball  would

suddenly swerve when half way to the batsman, which was too  late

for most of them to do anything about it.

This, incidentally, is why cricketers are constantly rubbing  the

ball up and down their crotches - they only ever polish one  side

of  the  ball,  leaving the  other  side

rough and mucky, so the flow is sure to be uneven.

The shapes with the lowest drag coefficients are teardrops. However, you can’t make a low-drag bike by trying to make it look like a teardrop.

Teardrops are fine shapes for tears, and not much else. They work

when  they  are  flying around in  undisturbed  air,  that's  why

airships are shaped like them. But they don't work when close  to

a flat surface (like the ground), they don't work in  crosswinds,

and  they certainly don't work with rotating tyres,  wheels,  and

brake  discs  sticking out of them. Oh, I nearly  forgot  -  they

don't work too well when running close to another shape which has

messed up the air around it.

It  is  possible  to design a nice smooth  shape  around  a  bike

chassis,  but  the rules - and the riders -  prevent  that  ideal

being approached.

Riders  need to be able to see where they are going, and to  have

things  like bars and pegs where they want them, not  where  they

are most aerodynamically efficient. What is also quite irritating

is that the riders will not sit nicely tucked up, but they insist

on  fidgeting  around,  hanging  their arses  off  the  side  and

sticking their knees out into the airstream. Remember the drag of

the  gloved  hand?  Think  of a  knobbly  knee,  slider,

leathers, and  boot.

This is actually not such a big deal, as of course when riders do

stick bits of themselves into the airstream like that, they could

not  go any faster anyway, they are already right on  the  ragged

edge.  The  only time during a lap that the  aerodynamics  become

important  is when the rider can be all tucked in with  his  head

flat on the tank and throttle against the stop.

Of course, a 125 rider will be able to do this for a much greater

percentage  of  a  lap  time than someone on a  500.  Even  on  a

megabike, however, these things can make a difference, especially

on  a  circuit  with a lot of  high-speed  flat-out  stuff,  like

Hockenheim or the Isle of Man.

I am a fully paid-up member of the Small Bikes Are Best

club. When the difference in average race speeds between the  500

and  125  GP winners can be as little as 6mph, I  would  hope

that  you can begin to see why, especially as the 125s  of  today

have  less  grunt  than was potentially available years ago  when  they  were

allowed   twin-cylinder   engines.  The   slightest   aerodynamic

advantage is worth a hell of a lot on these machines - that  1bhp

gloved hand makes a big difference when you only have 38 or so in

the first place.

This also goes to show you how much extra braking force you can get by

sitting  upright  at the end of the straight. Think  of  it  like

this; suppose you need 175bhp to run flat out at 190mph, then  if

you close the throttle you must have, in effect, 175bhp worth  of

force slowing you down at that speed. Just suppose that the power

required  to  do  190 sitting up is about 250bhp,  and  you  have

nearly half as much drag again. Better than that, the drag  force

acts  high up on the bike, which does a little to keep  the  back

end  from  lifting as it tries to rotate around the  front  wheel

contact patch.

Think of an F1 car with its 750bhp and Cd about double that of  a

housebrick  -  get  off the throttle at 190,  and,  without  even

touching the brakes, you will slow down faster than a bike can do

an emergency stop.

On the basis of the limitations outlined above, you would suppose

that the most you could hope for would be to make a bike body  as

smooth  and as slippery as possible, so as to reduce the size  of

the  wake  dragged around behind it and  keep the Cd  low.  Small

wakes  mean that following riders get much less of a  "tow"  when

they are slipstreaming, of course.

This  is certainly not easy, as the large part of a  bike's  body

suffers  by  being downstream of the turbulence  created  by  the

front   wheel.   Wheels   are  very  difficult   to   deal   with

aerodynamically, that's why sports cars have much lower drag than

single-seater  type racing cars.

F1  cars have all sorts of funny shaped bits of body  around  the

wheels  to try to stop the turbulence from upsetting  things  too

much,  because  the rules say that you can't  enclose  them.  All

attempts  on  bike outright speed world records in  recent  years

have been made using bodywork which completely enclosed the front

wheel area.

The  external  surfaces  of  a  vehicle  often  get  all  of  the

attention,  with  the  result that really  vital  internal  flows

(through radiators, engine air intakes, brake cooling ducts, etc)

are neglected.

The  first  Harris  and ROC GP bikes were awful  in  this

respect, with their carburettor air intakes cunningly designed so

as to take some of the hot air spilling out over the radiator and

most  of  the powdered carbon, bits of rubber, and  other  debris

coming off the front wheel.

Now,  given that you can wave goodbye to about 1% of your  engine

power  for every 5 centigrade rise in the temperature of the  air

which  is  fed to it, you wonder how the bikes ran  at  all  with

carbs  so  stinking hot that you could barely hold your  hand  on

them in the pits.

During early season testing with Neil Hodgson's RS125 a few years ago, the eagle-

eyed engineer of the Roger Burnett team, Steve Thompson (who  was

no slouch on a bike himself until retiring from racing the  year before)

noticed  that  the data logger readout of  the  carb  temperature

showed  that  it was running quite hot with Neil  all  tucked  up

along  the straight, but dived by 5 degrees when he sat up  under

braking. Armed with this knowledge and the data logger, a  better

airbox was developed.

Radiator ducts are a thorny problem. In theory, it is possible to

make them produce some useful thrust instead of drag. After  all,

they  are just  pipes with heat energy added inside, and that  is

how a jet engine works, isn't it? Bike designers have not  caught

up with this one yet.

I  once did some work  involving the  use of a 1989 Formula 1 car as a test bed. It produced about  600bhp, and had a radiator not much bigger than a GP bike's. The  cooling system  could  dissipate four times as much heat as the one  on  a

bike  because the person designing it knew what he was  on  about

(and remember that cars spend a much greater proportion of a  lap

producing   their   maximum  power  and  needing   maximum   heat

dissipation). Unlike most racing bike designers, he also realised

that  it wouldn't be a good idea to blow the witheringly hot  air

coming out of the other end all over the driver.

This design of radiator housing has been available for all of the

bike  engineers to come and see for four years, but not one has even  bothered to look.

Aerodynamics is a real free-for-all in bike development now. Real

gains  are there to be had for anyone with the brains to  read  a

few books and the application to try a few ideas. You don't  need

to  pay a gorilla and a half daily for a space-age  wind  tunnel,

significant progress can be made by  trial-and-error, going up and down the road (or better still a  disused runway in the early morning when the air is calm), especially  if

you  have  a  data  logger  to  monitor  pressures,  speeds,  and

temperatures accurately.

Even if you don't have a logger, you can make big improvements by

using  your  head  and keeping your eyes on the  way  road  grime

leaves patterns, or you can stick woolly tufts to the bodywork in

important areas, or run manometers into ducts, etc.  I have  done

this  on  everything from  racing karts to 38  tonne  articulated

lorries. The lorry end of things is big business, by the way.  If

you  can  reduce  the  drag by 30%,  then  you  reduce  the  fuel

consumption  by 10%. Then you go and tell someone like Boots  the

Chemists  -  they  spend  £8 million on  lorry  fuel  every  year.