CHASSIS DESIGN

A classic way for a design engineer to keep out of  trouble

is to stick to accepted ideas and never do anything too  radical.

After all, if you just do a pretty straight copy of a design that

you already know works well, you are shortening the odds  against

a cock-up quite dramatically.

I  regard this as a perfectly legitimate tactic, on  the  grounds

that  there are many unknowns in engineering, and the stakes  are

very high for even the most trivial jobs - I don't want to be the

one  who designed the bung which blew a gasket which put  oil  on

the rear tyre which caused an accident which killed someone. This

is  a heavy responsibility, I can tell you.

If you stick to what everyone else is doing, you are likely to be

pretty  safe,  but  you will also be a  boring  fart.  Let's  face  it, if you want to be average at your job,  you  can only  get to the top as a politician or as a sheep.

The herd instinct can be so strong in design engineers that  they

stick to certain ideas which are well past their sell-by date.  I

propose  that  the twin-spar chassis frame is one of  these,  but

that  designers are blinded by its near-universal popularity  and

they  don't want to use an open-minded approach to find a  better

answer.

One of the reasons behind this is precisely that the structure is

a  bike  chassis, and this brings out  pre-conceived  ideas.  So,

instead  of thinking about bike frames, just think for  a  moment

about structures in general, and what they are required to do.

Any  sort  of  chassis structure must hold things  in  a  certain

position  in space, under the influence of external forces  which

might be fairly constant (like gravity) or changing (like someone

sitting  on it). The way it is built is decided by the nature  of

the forces, how much money there is to spend, how small and light

the chassis must be, etc.

A bridge is a classic chassis structure. It must support its  own

weight,  and that of stationary or moving traffic on it. It  must

be  quite rigid (not because of structural aspects,  but  because

punters  won't  want to cross a bridge that moves about)  in  the

face  of  floods, winds, earthquakes, etc, etc. As  it  does  not

matter  too  much about how big and heavy it is, the  chassis  is

often made mainly of concrete (which is strong in compression and

cheap)  and steel (which is used only for the bits which need  to

be strong in tension, as it's relatively expensive).

Aircraft  and  ships are structures which must enclose a  lot  of

space (to house fuel and cargo) and must resist bulk forces  (air

or water pressure) acting on them, and so their chassis structure

is of the monocoque, stressed-skin, or "shell" type. Since planes

must  be light to cut down on fuel bills, and so they  can  carry

more cargo, they are built of expensive metals (steel,  titanium,

aluminium)  and/or  composites (fibre  reinforced  polymers).  It

doesn't  matter much how heavy a ship is, so you can build it  of

low-grade steel and concrete. Concrete? Yes, sometimes.

As  a general rule, any sort of structure will become more  rigid

the  further  the  bits that make it are  from  the  centre.  The

ultimate  expression  of  this is the shell, which  is  great  at

resisting  bulk loads, but by spreading the material  too  thinly

you  affect  its  ability to resist point  loads.  If  there  are

concentrated  loads around, you need a framework to resist  them.

Shell structures, when used appropriately, are very strong.  They

are just the job for chassis which must resist bulk forces.  When

a hen sits on her nest, her fat feathered backside is applying a bulk

load to her eggs, which must house a liquid without cracking.  It

is  practically impossible to break an egg by crushing it in  the

palm  of your hand (which is a bulk loading); the only way to  do

it is my cheating and applying point loads with your fingertips.

This is why a hen's egg has a shell-like structure (no,  really).

Things  like  eagles'  wing bones are  actually  composite  space

frames  inside, because they have to take the concentrated  loads

of the tendons.

Nature  has  taken years of evolution to show us  that  shell  or

monocoque  structures  are  to  be  used  for  bulk  loads,   and

spaceframes  for concentrated loads. It's obvious really; even  a

thrush knows that he can't break a snail's shell by crushing  it,

so he beats the shit out of it on a rock. Now given that a  twin-

spar motorcycle chassis is really a box-structure trying to be  a

crude  monocoque, just where are the bulk forces which it has  to

resist?

As  far  as the chassis is concerned, an engine is not  really  a

lump,  but  a series of concentrated loads, applied  through  the

bolts  that  hold it in. There are only three bolts  holding  the

engine in my RS125, and five in my Fireblade.

The  rear  swinging arm is likewise two point  loads  (where  the

bearings  are), and so is the front end, because all  the  forces

must go into the chassis through the head bearings. This  applies

to  funny front ends as well, they all pivot around  bearings  on

the chassis somewhere. Funny rear ends, by which I mean all sorts

of complex monoshock linkages, are pretty much the same as far as

a chassis structure is concerned.

In fact, the only bulk loads are air pressure (but the fairing is

held on by point-load nuts and bolts), fuel (but the tank is also

fixed  with point loads) and the rider's arse. All of these  bulk

forces  are very small, as far as the chassis is concerned.  This

is why Aprilia make a carbon-fibre reinforced polymer shell  seat

structure,  but attach it to the rest of the bike with four  nuts

and  bolts. What they are doing is turning a bulk load into  four

point loads.

So the obvious way of making a bike chassis is to connect all  of

the  point loads up with straight tubes welded together. Where  a

tube  looks  like  it might be so long that  it  could  bend  and

buckle,  the middle can be supported by triangulating it  with  a

couple of others. If this sounds too simple to be effective, take

a  look at the way the crane system used by the space shuttle  to

recover  satellites is made. If it's good enough for NASA,  there

can't be too much wrong with the concept.

Tubes  should  never,  ever,  be  used  to  take  bending  loads,

therefore  you should never see a curved tube on a  chassis.  The

reason  for this is easy to demonstrate. Just take  the  lightest

bit  of mild steel tube that you can find (or copper water  pipe,

that  will do) and try to stretch it end-to-end with your  hands.

You  can't do it, and neither could  the world's  strongest  man. He couldn't compress  it  along  its length either, unless it was so slender that it buckled. But  how

about  bending  it  by pushing sideways against  the  middle?  He

could, I could, pretty much anyone could.

Whenever you see curved tubes in a frame, or straight tubes which

are  obviously  taking bending loads, you are looking at  a  poor

design. It's such a shame to reduce the effectiveness of a  piece

of tube by a factor of ten (easily) just by putting a bend in it. (Fig 1).

Some  Ducati space-frames are very badly designed, carrying on  a

fine Italian tradition of badly designed chassis frames which can

be  traced through various Ferraris and all the way back  to  the

Alfa Romeo P3. The racing Ducati 851 frames were almost devoid of

bent  tubes,  unlike  the modern road bikes,  and  I  can't  help

thinking  that the famous composite structural airbox on the  916

wouldn't be necessary if only they had made the frame properly in

the first place. Compare and contrast with the steel tube trellis on the MV Agusta F4.

You  don't  have to be Italian to make a pig's ear of  a  tubular

chassis, the Japanese have made a perfectly good job of it in the past on the

Suzuki  GSX-R  bikes  with their twin-loop  cradle  frame.  This  is

basically  an aluminium tube perimeter structure trying  to  look

like a twin-spar set-up; not only is it bent pretty much all  the

way  round, but it also (horror of horrors) has bolted joints  so

that  you  can  get the engine out. Nothing cocks  up  the

rigidity of a chassis quite so much as a bolted joint or two.

The saving grace of the Suzuki chassis is the engine, which is so

big and strong that it covers up most of the frame's  weaknesses.

The chassis is really just a series of brackets to hang bits  off

the  engine. Ducatis use their engines in a similar way - a big lump

of aluminium to stop all of the flimsy tubes bending about.  Most

single-seater  racing cars don't have any chassis at  all  behind

the driver - all the loads are fed through the engine.

This  concept is similar in a way to the Bimota Tesi.  The  omega

chassis  around the engine is really just a bracket  for  hanging

the  suspension  off - nothing wrong with  that.  But  everything

else,  like the seat unit and the handlebar mount, is held  by  a

steel tube spaceframe which looks like it was designed by one  of

these  boot-faced saggy-arsed lesbian modern art types who make  welded  steel

sculptures  because they like wearing leather aprons and  foundry

boots.  A decent designer could have made it twice as  rigid  for

half the weight.

Rigid  structures are made out of tubes by joining them  together

as  lots  of  triangles. Squares should never  be  used,  because

squares  will  squash out of shape or "lozenge" if  you  lean  on

them.  Triangles  won't. It is usually easy to turn  a  rectangle

into  two  triangles by putting a diagonal brace  in.  A  classic

triangulated  structure is something like the jib of  a  building

site crane, or an electricity pylon.

A  well-designed  tube  chassis shouldn't  need  any  reinforcing

gussets  or plates around the joints, as there shouldn't  be  any

flex  in there anyway (Fig 2).

When analyzing the flexure of  spaceframes (normally  by a theorem called "virtual work" which  sounds  like just  my  cup of tea) it is assumed that all the joints  have  no

strength  at  all. This is what an engineer is on about  when  he

refers to a "pin-jointed structure".

The  best  way  of joining steel tubes is  by  a  low-temperature

brazing  process; I am a particular fan of the Sifbronze  welding

system  which  I believe was patented by BOC. This  is  how  most

lugless-framed racing push-bikes are made, and also racing karts,

which have to take a huge amount of stick through their joints as

they  don't have any suspension to filter nasty road shocks  out.

As  we  are seeing more and more glued joints  in  metal  chassis

construction these days, it might not be too long before  someone

tries this on a bike spaceframe (the MZ Skorpion doesn't count as

it's not a true spaceframe, it's a twin-spar with the spars  made

of bent tubes).

One  of the great advantages of a spaceframe is that  it's  quite

easy  to calculate exactly what the stresses and strains  are  in

each  part of the structure, and therefore to make sure that  the

tubing used is the lightest that you can possibly get away with.

The only way to know the forces and deflections in a monocoque or

spar-type  structure  is  by  the  process  of  "finite   element

analysis"  which  requires  a  bytemungous  amount  of   computer

processing power, and often isn't very accurate unless the design

engineer concerned has a very firm grip on what data is fed  into

the  calculations.  How many computer programmers are  needed  to

change  a  light bulb? None; it can't be done - it's  a  hardware

problem.  Most  people just build a chassis, then  see  where  it

cracks,  then  make the next one a bit beefier  there.

So  if a spaceframe is the way to handle point loads, why  aren't

F1  cars  made like that? After all, loads don't come  much  more

pointy  than  wishbones on to rose joints, do  they?  Well,  most

racing  cars  do actually have space frames, but  you  can't  see

them.  The front suspension loads are fed into two  small  frames

inside  the body, which are basically made up of  hollow  struts,

machined from a solid billet of aluminium or magnesium, depending

how  much  wonga is available.

Cheapo racing cars (like Formula Fords) have these frames made up

of  welded  steel tubes. They are normally  located  slightly  in

front,  and  slightly  behind, the  driver's  feet.  I  always  wore karate shin pads when driving because it  hurts  like hell if you bang your legs on 'em.

The problems come further back; the driver and the fuel cell  are

large  bulk  loads,  and  you  can't  make  a  nice  triangulated

structure  because  you can't pass chassis  tubes  through  them.

Actually,  there  are  one or two racing  drivers  that  I  would

cheerfully  pass chassis tubes through but that, as they say,  is

another story.

In the event of an accident, you don't want broken tubes spearing

the  driver or the fuel tank, so it's better to  follow  aircraft

practice  for your bulk loads and go for a  monocoque  structure,

which  you then stick around the front spaceframes,  thus  hiding

them from view. Rear suspension loads, incidentally, are normally

fed straight into the gearbox casing.

If  your bike has a tubular frame which is less than  brilliantly

designed,  you can beef it up by either putting extra  struts  in

(the preferred method) or by welding strengthening gussets around

the  weakest  joints.  To avoid adding  unnecessary  weight,  you

really  need  to  find out exactly where the  extra  strength  is

required.

There is a very easy way to measure torsional chassis flex. What you do  is

to  fix the headstock rigidly (by putting a steel rod through  it

and  welding that to an old bit of railway, or  something),  then

stuff  a  long bar through where the rear spindle  goes,  or  the

swinging-arm  fulcrum.  Put  a  heavy  weight  (your  girlfriend,

normally)  on the end of this bar, and measure the deflection  on

the end.

By getting your girlfriend to bounce up and down on the bar, you can see  which

bit  is  flexing,  and do something to stiffen it  up. This will be seen as a smaller  deflection  on the end of the bar.

Don't get too alarmed at the amount of flex you can see; even  if

your girlfriend only weighs 50kg or so, she will put a hell of a

lot more twist into the frame by hanging on to the end of a  six-

foot  bar than any tyre force with a leverage of a few inches  or

so  will manage. The forces going into bike frames are  generally

not  very big, anyway, because they put a lot less rubber on  the

road than the average car, and there's no aerodynamic downforce to speak  of,

which  is  how  a  racing car gets its  grip  and  generates  its

cornering force.

Given  that a motorcycle chassis is really just a  collection  of

point  loads to be held together without flexing, I am  genuinely

surprised that all GP bikes are not made of steel spaceframes. It

seems  to  me that steel tubes are not only  the  best  technical

solution,  they are also relatively cheap, and easy to work  with

and  repair.

The  notion of a spaceframe is not exactly a new, risky,  untried

adventure  - you only have to look at anything from  the  Ducatis

(whose design leaves a lot to be desired) to the Thrust2 jet car,

which  did 633mph on a chassis made of TI Reynolds' finest -  and

they  even modified it before the run, using portable welders  in

the  middle  of  Black  Rock  Desert.  That's  my  idea  of   top

performance  and  practicality with it; but  perhaps  steel  just

doesn't seem flash and modern enough these days.

I'm  not trying to make out that the aluminium spars  don't  have

their  advantages (and here I'm dismissing deltabox designs as  a

cheap,  mass-produced substitute). The designer who is  committed

to aluminium has a much greater freedom in how his components are

made,  for a start. The great boon of this material is  that  you

can  butt an extrusion up against a casting, put a  forging  over

the  top,  and weld the lot together. This can be  a  big  relief

around  the  swingarm  pickup area, or the  steering  head.  With

steel, you don't have that sort of range of choice, and this puts

a  premium  on design expertise to stop  everything  getting  too

heavy.