DYNAMOMETERS

Engine  performance  and evaluation is an  involved  and  complex

subject;  the  reason I find it so fascinating is that  there  is

still  a  lot  of  guesswork involved,  especially  if  you  have

less  than £2m to spend. The problem with anything like  this  is

that  once  guesswork gets its toe in the door,  opinion  follows

immediately  and ego soon after that. So getting two  dynamometer

manufacturers  in  the same room can be rather  like  watching  a

cock-fight or a parliamentary  debate. It is so sad to see engineers sink to  the

level  of politicians.

Dynamometers  are  a process, not a result. When people  say  "we

want a dynamometer" they don't really mean it, they mean "we want

to know about the performance of our engine" which is a different

thing  entirely.

The  differences between a process and a result are  not  readily

appreciated  in  engineering  for some reason,  but  people  like

advertisers  know  all  about them. They  never  say  "wash  your

clothes  with our fabric conditioner" (process), they  say  "your

clothes can be softer and fluffier and fresher than ever  before"

(result).

The big problem with knowing what your engine is doing is that it

is  heavily influenced by outside factors which change from  hour

to  hour.  Despite what the manufacturers might  claim,  no  dyno

currently available, at any price, will correctly mimic racetrack

conditions  during  engine tests. Just look at  Honda,  who  were

reputed to be spending £150m per year on their F1 engine  project.  How  did  they  fine-tune  things  like  inlet trumpets  and exhaust systems? By bolting them on the car  for  a few  laps  and looking at the telemetry, of course. There  is  no

substitute for this, dyno tests are a poor second best, even  for

Honda F1.

So  why use a dyno at all, rather than an on-bike data logger  to

get to the result?  It's because the process of testing on a dyno

is  much more agreeable than doing it on a track. You don't  have

to load the truck up at the first sparrow fart to drive 50  miles

in order to spend several hundred quid standing in a freezing pit

garage  looking at the pissing rain.

You  can easily spend more on a data logger than on a  dyno  (and

it's a waste of time going without a logger), so why not stay  at

home in the warm and dry? That way you can at least guarantee  to

get  a test on the engine. Going to a track means that you  can't

help testing the weather, the chassis, the tyres, and the rider as well.

It  was  the  world  of  formula  1  cars  which   revolutionised

dynamometer  design  around  the early  1980s.  Until  then,  the

preferred testing kit was something like a Froude G490  hydraulic

unit,  a  great bit of kit but substantially the same  as  all

hydraulic dynos made for the previous five decades.

These  dynos work by using a type of water turbine  to  dissipate

power. The amount of power can be set so that it exactly  matches

that  of  the  engine,  when the  speed  is  therefore  perfectly

constant  and the power can be worked out from the speed and  the

torque on the turbine housing. A gate valve  with a sophisticated

control system on the water supply varies the speed at which  the

engine  is held, so a series of power readings can be plotted  up

the rpm range.

Froude  were very much the IBMs of the hydraulic dyno game,  they

had  their imitators in the form of companies like  Go-Power  and

Superflow  who were really the Amstrads and Compaqs of  the  dyno

world.  But  they sold perfecly good systems which were  easy  to

install and operate.

Note that power is a dynamic thing, and therefore very  difficult

to  measure. In the days before the electronic revolution,  power

could  only  be measured by separating it into  components  which

could  be  seen and measured much more easily -  like  speed  and

torque, or volts and amps if you wanted to do it electrically.

It was only when the formula 1 crowd switched to turbo engines in

the  mid 1980s that they realised that their testing methods  had

been totally wrong for so long. There had always been a suspicion

that  there were odd engines that went really well on the  track,

but  poorly on the dyno (and vice versa), and the  turbo  engines

made this so much more obvious. As anyone who has ridden a  turbo

bike will know, the ultimate power of one of these things is  not

half  as  important as the response - how fast it  gets  to  that

power.

It suddenly dawned on the engineers that measuring  steady-state,

constant  speed power output was a waste of time. After all,  the

engine  was only required to perform like this for the  last  ten

yards  of  the main straight. For the other 98% of the  lap,  the

turbine  was  trying  to keep up with the  engine  and  the  fuel

injection  system was chasing them both like a  headless  chicken

during   acceleration,  and  of  course  gearchanges  and   brake

applications  were like throwing a spanner into the whole  works,

with  the  boost  and turbine speed up and down  like  a  whore's

drawers.

So why test a racing engine under steady-state conditions that it

would  never  see on the track? It's just like picking  the  best

high-jumpers in an athletics club to enter the mile run. This  is

not a bad analogy, as another problem with measuring things in  a

steady-state  way  is  that most  highly  tuned  racing  engines,

especially two strokes or four stroke turbos, do not like running

at constant speed and max power for any time. At best, the  power

might  just fall away as they get hotter, meaning that  you  will

end  up  with  weird (over-rich) fuel  settings  which  would  be

unsuitable  for  the track. At worst, things will  just  go  into

terminal meltdown.

Experienced  engine tuners developed a flair for setting  engines

up  not  necessarily for maximum power on the dyno,  but  on  the

track.  For example, an air-cooled two-stroke for a bike  with  a

fairing might be set well rich on the dyno to keep it cool on the

track  for best performance, whereas a liquid-cooled  four-stroke

might  be  set up well-lean as it would be cooled better  in  the

face  of  a  150mph wind. Then again, if  it  had  a  ram-charged

airbox,  the tuner would prefer to see it a bit rich on the  dyno

at the top end.

The  preferred way of doing this is with an exhaust gas  analyser

to tell you what the mixture is doing. You really need to keep an

eye on carbon monoxide, carbon dioxide, and unburnt  hydrocarbons

to get the best results, but just monitoring the carbon  monoxide

and the exhaust gas temperature is not a bad second best. The big

problem here is that gas analysers have very slow responses,  and

by  the  time  they have settled down to a  proper  reading,  the

engine will have melted.

Note that all of the above measures involve setting up an  engine

according  to  a  tuner's experience, not to  the  maximum  power

settings on the dyno. So why have one at all?

A  partial solution is to try to get the dyno to mimic  racetrack

conditions  more  closely.  Superflow and  Go-Power  developed  a

control  for  their  hydraulic dynos which allowed  power  to  be

tested  under  constant acceleration (called a  ramp  mode  test)

rather  than constant speed, or by rapidly jumping from  one  rpm

reading  to  the next (step mode) but this is  still  not  really

approaching race conditions.

Much   more  flexibility  of  control  was  available   to   dyno

manufacturers who used electrical methods to dissipate the power.

Highly respected names who play at this game in the racing  world

include  people  like Test Automation in Worcester, England,  and  foreigners

like Borghi e Saveri, Bosch, and Schenck.

The  advantage of electrical dynamometers (broadly three types  -

DC or AC generative or eddy current) is in their controllability,

normally  by computer. So you can program in steady-state,  ramp,

or  step tests, or get the dyno to mimic the road-load of a  bike

or car to drive the engine around through gear changes and on/off

throttle  conditions to find out what it would do coming  out  of

corners.

Disadvantages centre around cost and ease of maintenance.  Decent

electrical dynos at the economy end of the market are still  frighteningly expensive, and they are not the sorts of things which  can be installed in your back shed on a Saturday afternoon.

There is a much cheaper way of getting a road-ish response from a

dyno,  which is to use an inertia (or impulse) type.  An  inertia

dyno is totally removed from the others so far discussed. Instead

of  having  a  system for dissipating the power as  fast  as  the

engine  makes  it, to measure its torque at constant  speed,  the

inertia  dyno is basically a large flywheel which  stores  energy

from  the  engine as it is accelerated. These things  are  crude,

nasty, and cheap - but they work.

Early  versions  of these things just had ways of  measuring  the

time  interval  between  two rpm settings,  but  with  the  ready

availability  of  cheap personal computers in  the  last  decade,

highly  sophisticated monitoring systems can be made  to  splurge

out power and torque curves instantly. Indeed, it is a very  good

option  to pick up one of these old dynos second-hand for  a  few

hundred  quid,  or  make your own, and then  retro-fit  a  modern

computer data acquisition system.

The  flywheel of an impulse dyno lends itself to being used as  a

roller  in a rolling road set-up. Rolling road  dynamometers  are

very  popular with bikers because you can just strap the  machine

on, and off you go, whereas conventionally you would have to pull

the  engine out of the chassis, make brackets to hold it  on  the

dyno, and all of the necessary throttle linkages, cardan  shafts,

electrical bits, etc.

There  is  no reason at all why a hydraulic  or  electrical  dyno

shouldn't  be coupled up to rollers for use like this; indeed  it

is the preferred system for testing rip-snorting (250bhp+) saloon

cars which would need rollers like millstones to store the energy

otherwise.

A  way of avoiding hassle with tyre wear or slippage during  bike

engine testing, without the bother of taking the whole engine out

to bolt it to a dyno, is to clamp the swinging arm, whip the back

wheel  out, and use an extra-long chain to connect up to  a  dyno

input  shaft. This method works a treat, but keep well  clear  of

the chain and make a decent guard for it.

There was some panic recently when a tyre manufacturer put out  a

scare  that running bike tyres on rollers could result  in  early

and  catastrophic failure, and that the only sure safety  measure

was to put on a brand new tyre after every rolling road  session.

On the basis that there might just be a hint of self-interest  in

this recommendation, several rolling road manufacturers and test-

houses  immediately started gobbing off about how safe they  were

really, etc, etc.

Wanting  a  proper opinion from someone who knew what he  was  on

about,  I  approached  a highly qualified  and  experienced  tyre

development  engineer and asked "can you give me a  detailed  and

cogent  scientific  background to these theories?"  and  he  said

"it's all bollocks" which was good enough for me. Apparently, the

tyre  industry themselves use roller-type rigs  extensively  when

designing  and testing new products, so rolling-road  dyno  tests

are hardly what the US constitution would call "cruel and unusual

punishment" for tyres.

There  are more rolling-road dynos available for hire  throughout

the length and breadth of this country than you can shake a stick

at, but unfortunately most seem to be dedicated to pushing tuning bits like exhausts, jet kits, and filters rather than the higher calling of independent scientific research. Because you depend on the dyno operator’s skill for the accuracy of the results, it is too easy for the crooks to fiddle the results so as to make their tuning parts look more effective.

Points  to note about getting meaningful results out  of  rolling

roads centre on repeatability. Dyno testing is all about spotting

little changes (maybe 1 or 2 bhp) in big numbers, so if the  same

set-up doesn't give the same answers every time, then you are (as

we engineers say) pissing in the wind.

If  you do a power run, then tighten the the holding-down  straps

two  clicks  on  the ratchet and try again, the  bike  will  have

probably  lost  2 or 3bhp due to rear tyre squidge. If  the  dyno

cell isn't well ventilated and the bike starts breathing its  own

exhaust,  it  will lose out badly (and so will  you).  Fluctuating

cell temperatures will lose it about 1% power for every 5  degree

rise,  assuming the engine temperature stays the same  (which  it

won't).

The  watchword  for  engine tests is  therefore  CONSISTENCY.  An

experienced  operator  will  develop  a  certain  rhythm, so that he starts every test  under pretty  much the same conditions. A big help with this is a  dyno

which  can  allow  for  changing  friction  at  the  wheel/roller

interface  (as  it  heats up, cools down, runs out  of  true,  or

whatever) and changing friction in the dyno itself.

If you do a test at 7am with stone cold bearings on the  rollers,

they  will have about 5% more friction than at mid-day  when  the

heating has been on for a while and the grease has been  loosened

up  and splashed around a bit.

When paying for a bike to be set up on a dyno, remember that  the

kit  itself is only a tool, just like a spanner. You are  relying

on  the skill and experience of the operator to do a  decent  job

with  it. If the operator looks like a bit of a tool himself,  go

elsewhere.

The  horsepower readings are not so important as the changes.  It

doesn't  really  matter if your  GSXRRR1800cc  turbonutternitrous

only  registers 80bhp when you arrive, providing you  are happy with how it feels and you leave  with 85.   Note  that  some dynos are open to  abuse  here,  favourite

tricks include the operator putting the air temperature sensor in

front  of  the fan for the first test, then shoving it  down  the

front  of  his pants for the last one, for  an  instant  5bhp

gain.

Always   distrust  power  figures  which  are   "corrected"   for

atmospheric  conditions. Correction factors don't,  period.  They

provide a rough guide at best, so you are much better off  trying

to do tests under the same conditions on the same day.

In  general, most bikes produce much less power than  is  claimed

for them. Don't be disappointed if you cannot get a power reading

anywhere near what it said in the catalogue, just concentrate  on

making  improvements  and making things  better  by  back-to-back

tests.